Polypipe Ventilation

Specification

for

Domus Radial Duct System

Next Generation 2014

Issue 1

Contents										Page

Scope of Works									3

Typical Specification 								3

Manufacturer									4

Product Range									4

Material										4

Size											4

Accessories										4

Configuration Options								5

Appendix A – Range Details							6

Appendix B – Installation Instructions						6

Scope of Works

Standard

MEV

A semi-rigid (Radial) duct system shall be used to aid in the extraction of stale air from all ‘wet rooms’ in a dwelling when connected through a manifold to a centralised mechanical extract ventilation system (cMEV) in accordance with the requirements of the Domestic Ventilation Compliance Guide 2010 edition.

Domestic Ventilation Compliance Guide 2010 edition specific references are:

Table 5, System 3 installation guidelines, 2.0 Ductwork, supplementary information

MVHR

A semi-rigid (Radial) duct system shall be used to aid in the extraction of stale air from all ‘wet rooms’ and the supply of fresh air to all ‘habitable rooms’ in a dwelling when connected through manifolds to a balanced mechanical extract ventilation with heat recovery system (MVHR) in accordance with the requirements of the Domestic Ventilation Compliance Guide 2010 edition and SAP 2005 & 2009.

Domestic Ventilation Compliance Guide 2010 edition specific references are:

Table 7, System 4 installation guidelines, 2.0 Ductwork, Supplementary information

SAP 2005 & SAP 2009: Specification requirements applicable to the utilisation of rigid duct performance data within the Standard Assessment Procedure (SAP) for dwellings with semi-rigid duct systems fitted to balanced whole-house mechanical ventilation systems (09.05.2012).

Example of MVHR Specification

A Polypipe Ventilation Domus Radial semi-rigid duct system shall be used to aid in the extraction of stale air from all ‘wet rooms’ and the supply of fresh air to all ‘habitable rooms’ in a dwelling when connected through manifolds to a Polypipe Ventilation Silavent HRX2 balanced mechanical extract ventilation with heat recovery system (MVHR), in accordance with the requirements of the Domestic Ventilation Compliance Guide 2010 edition and SAP 2005 & 2009.

The individual manifold connections shall be (a maximum of) twelve radial ducts and one top-entry circular appliance connection duct. Unused radial duct connections shall be plugged.

The radial ducts shall be insulated in accordance with the Domestic Ventilation Compliance Guide 2010 edition. For further information please contact Polypipe Ventilation’s Technical Team on 08443 715523 or email vent.tech@polypipe.com.

Manufacturer

Polypipe Ventilation

Product Range

Domus Radial

Materials

Manifold: Injection-moulded Expanded Polypropylene (EPP) and zinc plated mild steel (black and self-colour respectively)

Duct: Polyethylene (blue outer, white inner)

Plenum: Polypropylene (black)

Size

Duct: 75mm outside diameter, 63mm inside diameter

Plenum: Twin connections. Female connection adapts from one or two 75mm ducts and male connection to one 125mm duct.

The manifolds: shall be configured as either twelve radial ducts and one top-entry circular appliance connection (top-entry model) or nine radial ducts and one rear-entry rectangular appliance connection (rear-entry model). Unused radial duct connections shall be plugged.

Top-entry manifolds: 125mm deep x 397mm x 397mm

Rear-entry manifolds: 125mm deep x 397mm x 421mm

Accessories

75mm plenum plugs (black polypropylene)

75mm radial duct retaining-clip (self-colour zinc plated steel)

75mm radial duct seals (for use with plenum)

75mm radial duct insulation (25mm glass-insulation- filled polyester-coated-aluminium inner and outer sleeve)

System expansions packs: RDSE1 for 150mm duct and RDSE2 for 125mm duct

Room expansion pack, RDRE1

FireBrake intumescent duct connector pack, RDD488

Configuration options

Hybrid solutions integrating rigid and semi-rigid duct

Appendix A

Range Details

MEV

RDK-CMXS Radial house pack with CMX MEV unit

MVHR

RDK-HRXS Radial house pack with HRX MVHR unit

RDK-HRXB Radial house pack with HRX Bypass MVHR unit

RDK-HRX2S Radial house pack with HRX2 MVHR unit

RDK-HRX2B Radial house pack with HRX2 Bypass MVHR unit

For more information visit: http://www.polypipe.com/ventilation/products/domus-semi-rigid-radial-duct-systems

Appendix B

Installation Instructions

Download from: http://www.polypipe.com/cms/toolbox/Domus_Radial_Duct.pdf